## Slide 1: Nordig PVR Lite Proposal
Nordig TV Recorder spec is too heavy to implement.
Is it possible to prepare a lighter version of PVR spec for IRD’s with internal/external storages?
What are the main expectations of an end user from a tv recorder?
  Setting a recording should be easy. One Touch Record, Setting timer from EPG(ESG), manual record entering date/time and duration.
  It should record required program completely without cutting from start or end of the program. Accurate Recording.
  Playback should be easy and pause, fast forward/fast rewind should be possible. Trick modes should be possible.
  Pause of live tv and continue after a short while would be very nice for a short break! Timeshift with trick modes should be possible.
Since spec is light this is not a full PVR, so different naming can be discussed! For example name can be TV Recorder Ready!
Detailed List of PVR requirements and comparison between PVR and light version listed in following pages.

## Slide 2: Nordig PVR Lite Proposal
 |  | PVR | TV Recorder Light
14 | NorDig PVR feature requirements |  | 
14.1 | Introduction - PVR | n/a | n/a
14.2 | General - PVR | M | M
14.2.1 | Recording File System | M | M
14.2.2 | Recording capacity | M | M
14.2.3 | Deletion of recordings | M | M
14.2.4 | Failed and incomplete recordings | M | M
14.2.5 | Save only the last number of episodes | O | O
14.2.6 | File system intact after update | M | M
14.2.7 | Limitations in local storage, interfaces, extraction and removable media for recordings (security) | M* | M*
14.2.8 | Disk management / de-fragmentation | M | O
14.2.9 | Safe margins | O | O
14.2.10 | NorDig Record Lists functionality | O | O
14.2.10.1 | Recording capacity and disk management for Record Lists | O | O
14.2.10.2 | Broadcast Record List Entry Point | O | O
14.2.10.3 | Presentation of Broadcast Record Lists | O | O
14.2.10.4 | Broadcast Record List Subscription and Un-subscription | O | O
14.2.10.5 | Presentation of Future scheduled BRL Recordings | O | O
14.2.10.6 | Presentation of Acquired BRL Recordings | O | O

## Slide 3: Nordig PVR Lite Proposal
14.2.10.7 | Limitations for External Media | O | O
14.2.10.8 | Management of Embargoed Content | O | O
14.2.10.9 | Management of Content Expiry | O | O
14.3 | PVR Recording |  | 
14.3.1 | General PVR recording | M | M
14.3.2 | ESG/EPG recording programming | M | M
14.3.3 | Series recording | M | O
14.3.3.1 | Series, record all episodes | M | O
14.3.3.2 | Series, record limited number of episodes for a series | O | O
14.3.3.3 | Series, only one instance/copy of each episode | O | O
14.3.4 | Split recordings | M | O
14.3.5 | Recommended events | O | O
14.3.6 | Alternative instance | O | O
14.3.7 | Accurate Recording | M | M
14.3.8 | Simultaneous recording (”view one + rec another”, ”two tuners”) | M | O
14.3.9 | Full service recording | M | M
14.3.10 | Trailer booking/Promotional Linking (optional) | O | O
14.3.10.1 | General | O | O
14.3.10.2 | Icon activation and deactivation | O | O
14.3.10.3 | Default Icon | O | O
14.3.10.4 | Image icon position | O | O

## Slide 4
Nordig PVR Lite Proposal
14.3.10.5 | Subtitling and display of image icon | O | O
14.3.11 | Back-to-back recording | M | O
14.3.12 | Timeshift recording | M | M
14.3.13 | Late Recording (”continous timeshift buffer”) | O | O
14.3.14 | Manual recording | M | M
14.3.15 | One touch recording (OTR) | M | M
14.3.16 | Automatic conflict handling | M | M
14.3.16.1 | Conflict during the time of programming a (individual, series or manual) recording | M | M
14.3.16.2 | Conflict occurring after the time of programming recording(s) | M | M
14.3.17 | Maximum length of recordings | M | M
14.3.18 | Recording of recently removed recordings | O | O
14.3.19 | Recording of parallel broadcast and simulcast (SD/HD, reg) | M | O
14.3.20 | NorDig Record Lists recording functionality | O | O
14.3.20.1 | Management of Content Grouping | O | O
14.3.20.2 | Content Acquisition | O | O
14.3.20.3 | Recording List Hierarchies | O | O
14.3.20.4 | Management of Content Versioning | O | O
14.3.20.5 | Metadata Changes Post Broadcast | O | O
14.3.20.6 | Unresolvable PushDownloadPrograms | O | O

## Slide 5
Nordig PVR Lite Proposal
14.3.20.7 | Use of Program Information | O | O
14.3.20.8 | Recording Conflicts | O | O
14.3.20.9 | Broadcast Record List Removal | O | O
14.3.20.10 | Broadcast Record List Updates | O | O
14.4 | Playback |  | 
14.4.1 | General | M | M
14.4.2 | Replay/Playback – trick modes | M | M
14.4.3 | Relative Synchronisation | M | M
14.4.4 | Simultaneous recording and playback | M | M
14.4.5 | Full service playback | M | M
14.4.6 | Resume Playback | O | O
14.4.7 | NorDig Record Lists management and playback functionality | M* | O
16.3 | User Preferences, Reset to factory mode,PVR recording priority, SD vs HD: HD | O | O
12 SI | TVA crids incl default authority (used for: unique id, alt instance, series, recommended, split rec, trailer…) | M | O
12 SI | Trailer booking (related content descr, related content table) | O | O
12 SI | Broadcast Record List (metadata descr, metadata pointer descr, TVA XML model/stream for broadcast record list) | O | O
13 EPG | PVR: 8day ESG/EPG (basic IRD min present/following) | M | M