## Slide 1: NorDig SSU
Background info and industry proposals for future SSU alternatives

## Slide 2: Definitions
SSU: System Software Update: IRD updates its complete software stack
Search: where an IRD searches known locations for information about any Software updates
Download: the action of downloading an software update, either from a broadcast or IP source. Does not include installation.
Update/Install: Installation of any downloaded software
Automatic: Where the search, download and installation is done without user intervention.
Manual: where the user initiates a search, download and installation procedure
OTA: Over-the-air (here any broadcast alt: terrestrial, satellite or cable)
OTA Notifications: IRD manufacturer utilises the OTA mechanism to send a message to consumers to advise that an update is available online.
OTN: Over the Network (typically via Internet)
Local/USB update: An update mechanism where consumers uses a local port, for example USB, to manually update the IRD software. The update will typically have been downloaded from the manufacturer’s website.
Connectable IRD: An IRD which has the capability to be connect to the Internet, typically via either a wired Ethernet connection or using Wi-Fi.
Connected IRD: A connectable IRD which is connected to the Internet.

## Slide 3: Status today
NorDig
  NorDig (Unified 2.5.1) mandates support for OTA
  Operators are not keen on transmitting OTA SSU image sizes >100MB
  However OTA is not used in reality for iDTV (since ~ 2011/2012)
    Operators still report frequent use for STB/PVR (especially operator branded devices)
    We understand that as more IRDs include connectivity functionality the image size is increasing, hence, in the long term OTA SSU usage will decrease.
DTG
  Allows Notifications for image sizes >100MB
  OTA still mandatory: OTA notification and/or complete SSU over OTA (search/SI + download)

## Slide 4: Partial Update
Partial updates are another update option which has been considered.
Historically, IRD software has been delivered as a ‘monolithic’ block and it has not been possible to update small sections of the code.
It has been proposed that an update mechanism where by small sections of code could be updated either by OTA or OTN.
Currently partial updates are not supported by IRD (TV) manufacturers for a variety of reasons:
  It is technically difficult to break architecture down into independent modules
  There is always some integration between modules and layers which means even partial download in a modern smart TV will be hundreds of MB in size.
  From an SQA perspective having to test and support many devices in the field with different versions of each software would be almost impossible to handle.
    With a monolithic software block, if customer A has software 123 and customer B has software 124 IRD manufacturers can more easily understand, advise and investigate.
    If same scenario with partial solution where RF,SI, EPG, HbbTV, IP, SSU, CI+ all can have different versions. You can have multiple different combinations in the field.
    Safest solution will be full update.
  IRD manufacturers only make SSU updates if there are critical issues to fix
  Partial upgrade would mean significantly increase test time before rolling out fixes which is not optimal for an urgent fix.
  (However “Smart-TV” today frequently update partial but only for their apps, which is not normally part of the IRD functionality/core software)

## Slide 5: Options
OTA search + OTA download (update_type 1 or 2)
OTA search + OTN download (update_type 3, SSU over the return channel)*
OTA Notification (OTA search) + OTN/local update (update_type 4, SSU over the Internet)
OTN search + OTN download
Local update (e.g. USB)
OTA Over the Air/broadcast (-T/-T2/-S/-S2/-C/-C2),
OTN Over the Network/broadband
* Update type 3 defined early y2000 when “connected” IRD where using dedicated return channel to operator instead of via open Internet. SSU group do not believe this is an option that anyone will use anymore and not proposed as option for the future.

## Slide 6: OTA search + OTA download
Technology is:
  Reliable, proven and well known:
  Legacy technology: (originated in NorDig from 1998)
    More practical alternatives available today.
  Able to reach all IRDs specifically the ones that are not connected
    Except where a TV sets is connected to an STB (the updates may not happen)
    OTAs will only reach IRDs where the broadcast platforms provides SSU playout (engineering channel)
  Implemented by all IRDs but not useable in practice for modern TV sets / Connected devices
    This is due to SSU image size having become too large to broadcast as file sizes routinely exceed 500MB to 1GB in size.
    Engineering channels normally offer limited capacity like 100kbps
  OTN is used regularly instead (especially for TV sets)
OTA Testing issues exist for very large images
  Significant engineering/certification resource is spent fixing issues each year

## Slide 7: OTA Notification + OTN/local download
Reach “all” IRDs
  Notifications would be able to reach all IRD’s that receive broadcast services
  Requires good Internet connection (or user could receive SSU software via post on a USB memory stick, requires that the user contact and register the IRD to the manufacture)
  Consequently OTA notifications may not resolve any fundamental users’ Internet limitations.
    Limitations include Internet speed/download limits / coverage
Based on DSMCC for the OTA notification
  Reuse same core DSMCC software code in the IRD as used by SSU for OTA download
  Notifications need software development and may/will require IRD to connect to network (Internet) once notification is issued
    Increases development time
    Impact on manufacturers network: unclear
  When would a Notification be issued?
    Assumed mainly used for critical corrections/debug
      Frequency of use by IRD manufacturers is expected to be low (probably less for TV sets than for STBs)
    Adding important functionalities (e.g. OTN), more likely for STBs.
    A non-connected IRD that is working correctly probably does not need a software update and is comparatively secure.
  A new testing scheme will be needed by CE manufacturers & operators
    This would then also need to be added to the NorDig Test Plan
  Reduces IRD test time & overheads
  Provides a potentially useful mechanism to communicate with customers

## Slide 8: OTN Search + OTN download
OTN search & OTN download functionality
  OTN = Over The Network
  Today’s connected IRD’s and TV’s typically form a secure IP (Network) connection with a server hosted by the device manufacturer.
  This link enables the IRD manufacturer to deliver software updates as required.
  This function is especially used to update online applications.
  It is still usually possible for consumers to disable automatic software updates in case they have bandwidth or download limitations.
Set-up (application)
  As IP connectivity becomes increasingly prevalent and important, the easy set-up and (automatic) configuration of an IP connection, typically by Wi-Fi, is becoming common place and forms part of the key set-up processes.
  Where a consumer chooses to not set this up, they will also lose access to any VoD type services supported by the TV and thus will not need any application updates.
Purpose
  In addition to the delivery of VoD services the TV will use the IP connection to query its software (OTN Search) and to
  This also helps with registering new devices, so consumers are strongly encouraged to connect their new devices.
Availability
  All connected TV will have an IP channel which can be used for this purpose because OTA updates for images sizes >100MB will be work
Testing
  The link is a proprietary connection and so will be carefully tested by manufacturers.
  This is a very critical feature of the TV because it enables manufacturers to add new features and functionality so this will be well tested prior to product launch.

## Slide 9: Illustration: General trend of SSU over the years
y2000
y2016
IRD SSU size (average)
# of IRDs connected
to Internet
# IRDs forced to support
OTA SSU (NorDig requirements)
# of IRDs using OTA SSU
time
# of connected IRDs using OTA SSU

## Slide 10: Operators’ view
Operators feel that OTA (complete or notification) provides a certain degree of security/comfort (to reach all IRD units, also not connected ones):
  But with the increased SSU image sizes, is no longer completely correct assumption for complete OTA (OTA search + OTA download) because no operator would permit a large image to be broadcast with reasonable/necessary bandwidth (or too high cost for IRD manufactures or too high cost of capacity in broadcast)
Operators view is that IRD support some kind of SSU
Operators wants certifications (verification) of that IRD really support SSU before they are put on the market (e.g. via NorDig testing)
Operators are concerned that if OTA UNT Notifications are not supported there will be no direct (on the TV) way to advise consumers that a critical s/w update is needed:
  This is correct but is it a valid concern?
    TVs which are not connected are highly unlikely to need a code update.
    A USB/on-line update will be available (typically).
    Consumers with no/slow/metered internet have the same situation as an unconnected TV.
    Today OTA & OTN are implemented by IRD manufactures – this is a well proven system – since the last few years – which according to trends will only improve.
    IRD manufactures can contact consumers by letter/e-mail/SMS… (where devices are registered).
    Software downloads will be available on-line.
    IRDs with smaller images can still use OTA.

## Slide 11: IRD manufacturers view:
In addition to OTA, an OTN-only approach can be an acceptable option for the NorDig market in 2018
Newer TVs and STBs are increasingly connected to the Internet
  New smart TV sets seems to have higher/slightly higher figures that actually are connected to Internet than STB.
Wi-Fi in IRDs is widely used – making connection easier
  2015: Significant proportion of TV and modern STB/PVRs connected to Internet (often already during installation process)
~50% of TV are then connected to STB via HDMI for the main viewing and so are not used on a regular basis, thus making the need for updates unnecessary and negating the impact of any potential critical issues
TVs which are not connected would be significantly less likely to need any updates (online apps would not need updating.)
Segmenting SSU (partial SSU) has been discussed earlier that it could in theory be a way to reduce SSU file size for OTA download (i.e. SSU that only incl IRD functions excluding other features) but has not been used and manufactures do not see this as a viable option for the future (see previous slide)
IRDs can still be updated by local interface (e.g. USB) – permitting consumers in areas with slow internet to download at their leisure. (The impact on metered users is unchanged)

## Slide 12: Benefits & Issues Summary (for OTN-only)
Eliminated testing of unused OTA functionality
Avoids development of new OTA Notification functionality which will have very limited use.
OTN/USB updates more appropriate for the future are well proven
Current OTA system is not workable in practice (due to large SSU file sizes), gives a false sense of comfort, has enabled a stable OTN/USB system to develop.

## Slide 13: Device Manufacturers’ Proposal
Add OTN (search + download) as option in NorDig (i.e. IRD manufacturers can choose OTA or OTN):
  OTN-only permitted where there is an viable alternative (USB)
    USB allows updates by post or online
  Complete OTA (search + download) and/or OTA Notification:
    Can be optional if OTN is implemented
    Some manufacturers may wish to provide Notification support
    Manufacturers may implement Notification as a communication channel but it would not require such expensive/formal certification
    For OTA notification alt avoid complex conditions like “only allowed for IRD w SSU size above 100MB”

## Slide 14: Overview: What is in use today?
Mechanism | TV set/Connected IRDs | STB/PVR (non connectable) | Comment
OTA (search + download) |  |  | Supported by all IRD but not used by connected devices (due to large SSU size) Testing issues (for large SSU sizes)
OTA Notifications + OTN download |  |  | - New alternative (not yet specified in NorDig) - Not implemented yet
OTN (search and download) |  |  | - Used by DTV/Connected Devices
Local (e.g. USB) |  |  | - May be supported by most IRD, viable alternative to complement OTN
n/a
n/a

## Slide 15: Device Manufacturers’ Proposal
# | Proposal: | Connectable IRD (e.g. hybrid IRD) | Non connectable IRD | NorDig IRD spec
1 | OTA search + OTA download (update_type 1 or 2) | Optional / not required | Mandatory | Specified
2 | OTA search + OTN download (update_type 3) very old modem alt, under discussion to be removed | Optional (remove?) | N/A | Specified but old
3 | OTA Notification (OTA search) + OTN/local update (update_type 4) SSU via Internet connection | Optional | N/A | Not specified but proposed
4 | OTN search + OTN download | Preferred | N/A | Specified very little
5 | Local (e.g. USB) | + #4 | Optional | Specified very little
Is it acceptable to have different options / requirements depending on the profile of the IRD?
  E.g. Hybrid/Connected IRD may use their network connection instead of the OTA
Propose IRD’s shall implement at least one of the following options:
  IRD’s which do not support OTA shall also support a fall back mechanism such as local download.