## Slide 1: Rationale for proposal 11 of the dHDR in NorDig

## Slide 2: ExCom request
NorDig ExCom Draft report of 2020.03.05:
  “Dynamic HDR, text draft (optional, IRD shall not be disturbed, if used then according w DVB)”
NorDig ExCom draft report 2010.10.19:
  “Excom decide to add into next NorDig IRD spec if dHDR is used then signaling shall be as DVB specified and IRDs shall not be disturbed by formats not supported. AP for NorDig T to prepare proposal”

## Slide 3: Participating Manufacturers proposal
Add:
  This specification does not include requirements for dynamic HDR. Any dynamic HDR metadata would be delivered to the IRD in accordance with ETSI TS 101 154 [26]. The NorDig IRD shall ignore HEVC SEI messages the IRD does not support.
Purpose: simply align with the ExCom request

## Slide 4: Concerns about alternate introductions (1)
Remove:
  Dynamic metadata HDR refers to Support for Supplemental Enhancement Information messages carrying one or more DMI formats conforming to sub-section 5.14.4.4.3.3.4 “Optional Supplemental Enhancement Information messages carrying DMI” is not required i.e. is optional. Any non DMI cognisant HEVC HDR UHDTV IRD shall be able to decode and present the service, even if DMI is in the bitstream (i.e. the IRD shall not be disturbed by DMI SEI messages not supported by the IRD
Reason:
  Covered by the proposed paragraph
  Unnecessary technical details. Repetition of the DVB specifications information, which can be found if the proposed paragraph is followed.

## Slide 5: Concerns about alternate introductions (2)
Remove:
  Note 2: DMI refers to HDR dynamic mapping information and is information associated with one or more frames of the video content as part of a DVB service that can guide dynamic mapping, as produced in a reference viewing environment or otherwise (as defined in ETSI TS 101 154 [26]).
Reason:
  DMI is defined in DVB, so this is already covered by the proposed paragraph
  As previous page is removed, the definition is of DMI is now superfluous.

## Slide 6: Concerns about alternate introductions (3)
Remove:
  Note: In the case that DMI messages are included in the bitstream, the NorDig Rules of Operation [61] require broadcasters to provide video quality from that bitstream to NorDig HEVC IRDs that do not support DMI at the level that can be expected from a bitstream that does not include DMI messages. DMI enables further enhancement of the video quality.
  <move to RoO> It is highly recommended that bitstreams that include DMI provide video quality at the level that can be expected from a NorDig HEVC IRD that does not support DMI, and that the DMI enables further enhancement of the video.
Reason:
  Not relevant for IRD
  Already added to RoO

## Slide 7: Concerns about alternate introductions (4)
Removed:
  or DMI message pass-through (if supported ).
  by using DMI (if supported)
Reason:
  How to support dHDR out of the scope of this specification and in opposition to ExCom request.
  Request is to ensure non-dHDR receivers are not going to be affected by dHDR signalling, which is covered in proposed paragraph

## Slide 8: Concerns about alternate introductions (5)
Remove:
  If a Nordig HEVC IRD supports one or more DMI formats it should be capable of switching seamlessly between bitstreams with different DMI formats and between bitstreams with and without DMI. If aFor NorDigG HEVC IRD supportings one or more of the DMI formats, then it shall handle dynamic switching should be handled as described in ETSI TS 101 154 [26] sub-section 5.14.4.4.3.3.4.2 “Dynamic switching between bitstreams with and without DMI”.
Reason:
  How to support dHDR out of the scope of this specification and in opposition to ExCom request.
  Request is to ensure non-dHDR receivers are not going to be affected by dHDR signalling, which is covered in proposed paragraph
  Broadcasters have so far not selected even one dHDR. This is even more of a remote requirement

## Slide 9: Concerns about alternate introductions (6)
Remove:
Reason:
  Information already covered in proposed paragraph
  In contradiction with ExCom request

## Slide 10: Why are these important issues?
Issue for manufacturers
  Technical overload when no technical information is required leads to technical support questions (broadcasters primarily)
  Details lead to expectations of support by manufacturers, regardless of commercial needs - Manufacturers will be expected to support everything
  Increased development costs
  No commercial interest
Issues for Consumers
  Increased costs of IRD for no commercial reason
  Confusion when there is no broadcast signal
 There is no added benefits at this time for the consumers, broadcasters and manufacturers to include the text proposed to be removed
Issue for Broadcasters
  Confusion when assessing the specs
  Confusion when they might not even understand what dHDR is
  Expectations that NorDig/Manufacturers will guide them towards dHDR, or some specific solutions, when they need to make their own evaluation
  Currently they have reported little interest at this time.
 Broadcasters should make the decisions to that they want to use dHDR (with their commercial priorities, and having checked that sufficient content is available to support this operation
 Broadcasters can already start introducing dHDR in their market with the current proposal